MH6211 Instruction Set

00	TEST		1  *	TEST OPERATION TEST MODE ONLY

01	NOP		1  2	NO OPERATION

02	AIM DIR	3  ?	AND IN MEMORY

03	OIM DIR	3  ?	OR IN MEMORY

04	LSRD		1  3	LOGICAL SHIFT RIGHT DOUBLE ACCUMULATOR

05	ASLD / LSLD	1  3	ARITHMETIC / LOGICAL SHIFT LEFT DOUBLE ACC

06	TAP		1  2	TRANSFER FROM ACC A TO CONDITION CODE REGISTER

07	TPA		1  2	TRANSFER FROM CONDITION CODE REGISTER TO ACC A

08	INX		1  3	INCREMENT INDEX REGISTER X

09	DEX		1  3	DECREMENT INDEX REGISTER X

0A	CLV		1  2	CLEAR TWOS COMPLEMENT OVERFLOW BIT

0B	SEV		1  2	SET TWOS COMPLEMENT OVERFLOW BIT

0C	CLC		1  2	CLEAR CARRY

0D	SEC		1  2	SET CARRY

0E	CLI		1  2	CLEAR INTERRUPT MASK

0F	SEI		1  2	SET INTERRUPT MASK

10	SBA		1  2	SUBTRACT ACCUMULATORS

11	CBA		1  2	COMPARE ACCUMULATORS

14	IDIV DIR   	2  6	INTEGER DIVIDE

15	FDIV DIR   	2  6	FRACTIONAL DIVIDE   (b = D/M, > a = D%M)

16	TAB		1  2	TRANSFER ACCUMULATOR A TO ACCUMULATOR B

17	TBA		1  2	TRANSFER FROM ACCUMULATOR B TO ACCUMULATOR A

18 	XGXY		1  4	EXCHANGE REGISTER X AND REGISTER Y

19	DAA		1  2	DECIMAL ADJUST ACCUMULATOR A

1A	XGDX		1	EXCHANGE DOUBLE ACCUMLATOR AND INDEX REG X

1B	ABA		1  2	ADD ACCUMULATOR B TO ACCUMULATOR A

1C	CPD IMM	3  5	COMPARE DOUBLE ACCUMULATOR

1D	CPD DIR	2  6	COMPARE DOUBLE ACCUMULATOR

1F	CPD EXT	3  7	COMPARE DOUBLE ACCUMULATOR

20	BRA		2  3	BRANCH ALWAYS

21	BRN		2  3	BRANCH NEVER

22	BHI		2  3	BRANCH IF HIGHER

23	BLS		2  3	BRANCH IF LOWER OR SAME

24	BCC / BHS	2  3	BRANCH IF CARRY CLR / BRANCH IF HIGHER OR SAME

25	BCS / BLO	2  3	BRANCH IF CARRY SET / BRANCH IF LOWER

26	BNE		2  3	BRANCH IF NOT EQUAL TO ZERO

27	BEQ		2  3	BRANCH IF EQUAL

28	BVC		2  3	BRANCH IF OVERFLOW CLEAR

29	BVS		2  3	BRANCH IF OVERFLOW SET

2A	BPL		2  3	BRANCH IF PLUS

2B	BMI		2  3	BRANCH IF MINUS

2C	BGE		2  3	BRANCH IF GREATER THAN OR EQUAL TO ZERO

2D	BLT		2  3	BRANCH IF LESS THAN ZERO

2E	BGT		2  3	BRANCH IF GREATER THAN ZERO

2F	BLE		2  3	BRANCH IF LESS THAN OR EQUAL TO ZERO

30	TSX		1  3	TRANSFER FROM STACK POINTER TO INDEX REGISTER X

31	INS		1  3	INCREMENT STACK POINTER

32	PULA		1  4	PULL DATA FROM STACK

33	PULB		1  4	PULL DATA FROM STACK

34	DES		1  3	DECREMENT STACK POINTER

35	TXS		1  3	TRANSFER FROM INDEX REGISTER X TO STACK POINTER

36	PSHA		1  3	PUSH DATA ONTO STACK

37	PSHB		1  3	PUSH DATA ONTO STACK

38	PULX		1  5	PULL INDEX REGISTER X FROM STACK

39	RTS		1  5	RETURN FROM SUBROUTINE

3A	ABX		1  3	ADD ACCUMULATOR B TO INDEX REGISTER X

3B	RTI		1 12	RETURN FROM INTERRUPT

3C	PSHX		1  4	PUSH INDEX REGISTER X ONTO STACK

3D	MUL		1 10	MULTIPLY UNSIGNED

3E	WAI		1 14	WAIT FOR INTERRUPT

3F	SWI		1 14	SOFTWARE INTERRUPT

40	NEGA		1  2	NEGATE

43	COMA		1  2	COMPLEMENT

44	LSRA		1  2	LOGICAL SHIFT RIGHT

46	RORA		1  2	ROTATE RIGHT

47	ASRA		1  2	ARITHMETIC SHIFT RIGHT

48	ASLA / LSLA	1  2	ARITHMETIC / LOGICAL SHIFT LEFT

49	ROLA		1  2	ROTATE LEFT

4A	DECA		1  2	DECREMENT

4C	INCA		1  2	INCREMENT

4D	TSTA		1  2	TEST

4F	CLRA		1  2	CLEAR

50	NEGB		1  2	NEGATE

53	COMB		1  2	COMPLEMENT

54	LSRB		1  2	LOGICAL SHIFT RIGHT

56	RORB		1  2	ROTATE RIGHT

57	ASRB		1  2	ARITHMETIC SHIFT RIGHT

58	ASLB / LSLB	1  2	ARITHMETIC / LOGICAL SHIFT LEFT

59	ROLB		1  2	ROTATE LEFT

5A	DECB		1  2	DECREMENT

5C	INCB		1  2	INCREMENT

5D	TSTB		1  2	TEST

5F	CLRB		1  2	CLEAR

60	NEG IND,X	2  6	NEGATE

63	COM IND,X	2  6	COMPLEMENT

64	LSR IND,X	2  6	LOGICAL SHIFT RIGHT

66	ROR IND,X	2  6	ROTATE RIGHT

67	ASR IND,X	2  6	ARITHMETIC SHIFT RIGHT

68	ASL / LSL IND,X	2  6	ARITHMETIC / LOGICAL SHIFT LEFT

69	ROL IND,X	2  6	ROTATE LEFT

6A	DEC IND,X	2  6	DECREMENT

6C	INC IND,X	2  6	INCREMENT

6D	TST IND,X	2  6	TEST

6E	JMP IND,X	2  3	JUMP

6F	CLR IND,X	2  6	CLEAR

70	NEG EXT		3  6	NEGATE

73	COM EXT		3  6	COMPLEMENT

74	LSR EXT		3  6	LOGICAL SHIFT RIGHT

76	ROR EXT		3  6	ROTATE RIGHT

77	ASR EXT		3  6	ARITHMETIC SHIFT RIGHT

78	ASL / LSL EXT	3  6	ARITHMETIC / LOGICAL SHIFT LEFT

79	ROL EXT		3  6	ROTATE LEFT

7A	DEC EXT		3  6	DECREMENT

7C	INC EXT		3  6	INCREMENT

7D	TST EXT		3  6	TEST

7E	JMP EXT		3  3	JUMP

7F	CLR EXT		3  6	CLEAR

80	SUBA IMM	2  2	SUBTRACT

81	CMPA IMM	2  2	COMPARE

82	SBCA IMM	2  2	SUBTRACT WITH CARRY

83	SUBD IMM	3  4	SUBTRACT DOUBLE ACCUMULATOR

84	ANDA IMM	2  2	LOGICAL AND

85	BITA IMM	2  2	BIT TEST

86	LDAA IMM	2  2	LOAD ACCUMULATOR

87	BRSET DIR	4	BRANCH IF BIT(S) ARE SET

88	EORA IMM	2  2	EXCLUSIVE OR

89	ADCA IMM	2  2	ADD WITH CARRY

8A	ORAA IMM	2  2	INCLUSIVE OR

8B	ADDA IMM	2  2	ADD WITHOUT CARRY

8C	CPX IMM	3  4	COMPARE INDEX REGISTER X

8D	BSR		2  6	BRANCH TO SUBROUTINE

8E	LDS IMM	3  3	LOAD STACK POINTER

8F	BRCLR DIR	4	BRANCH IF BIT(S) ARE CLEAR

90	SUBA DIR	2  3	SUBTRACT

91	CMPA DIR	2  3	COMPARE

92	SBCA DIR	2  3	SUBTRACT WITH CARRY

93	SUBD DIR	2  5	SUBTRACT DOUBLE ACCUMULATOR

94	ANDA DIR	2  3	LOGICAL AND

95	BITA DIR	2  3	BIT TEST

96	LDAA DIR	2  3	LOAD ACCUMULATOR

97	STAA DIR	2  3	STORE ACCUMULATOR

98	EORA DIR	2  3	EXCLUSIVE OR

99	ADCA DIR	2  3	ADD WITH CARRY

9A	ORAA DIR	2  3	INCLUSIVE OR

9B	ADDA DIR	2  3	ADD WITHOUT CARRY

9C	CPX DIR		2  5	COMPARE INDEX REGISTER X

9D	JSR DIR		2  5	JUMP TO SUBROUTINE

9E	LDS DIR		2  4	LOAD STACK POINTER

9F	STS DIR		2  4	STORE STACK POINTER

A0	SUBA IND,X	2  4	SUBTRACT

A0 80 SUBA IND,Y	2	SUBTRACT

A1	CMPA IND,X	2  4	COMPARE

A1 80 CMPA IND,Y+	2	COMPARE WITH/Y+

A2	SBCA IND,X	2  4	SUBTRACT WITH CARRY

A2 80	SBCA IND,Y	2	SUBTRACT WITH CARRY

A3	SUBD IND,X	2  6	SUBTRACT DOUBLE ACCUMULATOR

A3 80	SUBD IND,Y	2  6	SUBTRACT DOUBLE ACCUMULATOR

A4	ANDA IND,X	2  4	LOGICAL AND

A4 80	ANDA IND,Y	2  4	LOGICAL AND

A5	BITA IND,X	2  4	BIT TEST

A5 80	BITA IND,Y	2  4	BIT TEST

A6	LDAA IND,X	2  4	LOAD ACCUMULATOR

A6 80 LDAA IND,Y+	2	LOAD ACCUMULATOR WITH/Y+

A7	STAA IND,X	2  4	STORE ACCUMULATOR

A7 80	STAA IND,Y	2	STORE ACCUMULATOR

A8	EORA IND,X	2  4	EXCLUSIVE OR

A8 80	EORA IND,Y	2  4	EXCLUSIVE OR

A9	ADCA IND,X	2  4	ADD WITH CARRY

A9 80	ADCA IND,Y	2  4	ADD WITH CARRY

AA	ORAA IND,X	2  4	INCLUSIVE OR

AA 80	ORAA IND,Y	2  4	INCLUSIVE OR

AB	ADDA IND,X	2  4	ADD WITHOUT CARRY

AB 80	ADDA IND,Y	2  4	ADD WITHOUT CARRY

AC	CPX IND,X	2  6	COMPARE INDEX REGISTER X

AC 80	CPX IND,Y	2  6	COMPARE INDEX REGISTER X

AD	JSR IND,X	2  6	JUMP TO SUBROUTINE

AD 80 JSR IND,Y	2	JUMP TO SUBROUTINE

AE	LDS IND,X	2  5	LOAD STACK POINTER

AE 80	LDS IND,Y	2  5	LOAD STACK POINTER

AF	STS IND,X	2  5	STORE STACK POINTER

AF 80	STS IND,Y	2  5	STORE STACK POINTER

B0	SUBA EXT	3  4	SUBTRACT

B1	CMPA EXT	3  4	COMPARE

B2	SBCA EXT	3  4	SUBTRACT WITH CARRY

B3	SUBD EXT	3  6	SUBTRACT DOUBLE ACCUMULATOR

B4	ANDA EXT	3  4	LOGICAL AND

B5	BITA EXT	3  4	BIT TEST

B6	LDAA EXT	3  4	LOAD ACCUMULATOR

B7	STAA EXT	3  4	STORE ACCUMULATOR

B8	EORA EXT	3  4	EXCLUSIVE OR

B9	ADCA EXT	3  4	ADD WITH CARRY

BA	ORAA EXT	3  4	INCLUSIVE OR

BB	ADDA EXT	3  4	ADD WITHOUT CARRY

BC	CPX EXT	3  6	COMPARE INDEX REGISTER X

BD	JSR EXT	3  6	JUMP TO SUBROUTINE

BE	LDS EXT	3  5	LOAD STACK POINTER

BF	STS EXT	3  5	STORE STACK POINTER

C0	SUBB IMM	2  2	SUBTRACT

C1	CMPB IMM	2  2	COMPARE

C2	SBCB IMM	2  2	SUBTRACT WITH CARRY

C3	ADDD IMM	3  4	ADD DOUBLE ACCUMULATOR

C4	ANDB IMM	2  2	LOGICAL AND

C5	BITB IMM	2  2	BIT TEST

C6	LDAB IMM	2  2	LOAD ACCUMULATOR

C7	BRSET IND, X	4	BRANCH IF BIT(S) SET

C8	EORB IMM	2  2	EXCLUSIVE OR

C9	ADCB IMM	2  2	ADD WITH CARRY

CA	ORAB IMM	2  2	INCLUSIVE OR

CB	ADDB IMM	2  2	ADD WITHOUT CARRY

CC	LDD IMM		3  3	LOAD DOUBLE ACCUMULATOR

CD 08	INY		2  4	INCREMENT INDEX REGISTER Y

CD 09	DEY		2  4	DECREMENT INDEX REGISTER Y

CD 1A	XGDY		2	EXCHANGE DOUBLE ACCUMULATOR AND INDEX REG Y

CD 3A	ABY		2	ADD ACCUMULATOR B TO INDEX REG Y

CD 8C CMPY IMM, Y++	4	CMPY INDEX REGISTER Y AND INCREMENT.

CD A3	CPD IND,Y

CD AC	CPX IND,Y

CD CE	LDY IMM	4  4	LOAD INDEX REGISTER Y

CD DF	STY DIR	3  5	STORE INDEX REGISTER Y

CD EE	LDY IND,X	3  6	LOAD INDEX REGISTER Y

CD EF	STX IND,Y	3  6

CD FE			4????

CE	LDX IMM	3  3	LOAD INDEX REGISTER X

CF	*****		3	?????  (4!!!!!)

CF	STOP		1

D0	SUBB DIR	2  3	SUBTRACT

D1	CMPB DIR	2  3	COMPARE

D2	SBCB DIR	2  3	SUBTRACT WITH CARRY

D3	ADDD DIR	2  5	ADD DOUBLE ACCUMULATOR

D4	ANDB DIR	2  3	LOGICAL AND

D5	BITB DIR	2  3	BIT TEST

D6	LDAB DIR	2  3	LOAD ACCUMULATOR

D7	STAB DIR	2  3	STORE ACCUMULATOR

D8	EORB DIR	2  3	EXCLUSIVE OR

D9	ADCB DIR	2  3	ADD WITH CARRY

DA	ORAB DIR	2  3	INCLUSIVE OR

DB	ADDB DIR	2  3	ADD WITHOUT CARRY

DC	LDD DIR		2  4	LOAD DOUBLE ACCUMULATOR

DD	STD DIR		2  4	STORE DOUBLE ACCUMULATOR

DE	LDX DIR		2  4	LOAD INDEX REGISTER X

DF	STX DIR		2  4	STORE INDEX REGISTER X

E0	SUBB IND,X	2  4	SUBTRACT

E0 80	SUBB IND,Y	2  4	SUBTRACT

E1 	CMPB IND,X	2  4	COMPARE

E1 80	CMPB IND,Y	2  4	COMPARE

E2	SBCB IND,X	2  4	SUBTRACT WITH CARRY

E2 80	SBCB IND,Y	2  4	SUBTRACT WITH CARRY

E3	ADDD IND,X	2  6	ADD DOUBLE ACCUMULATOR

E3 80	ADDD IND,Y	2  6	ADD DOUBLE ACCUMULATOR

E4	ANDB IND,X	2  4	LOGICAL AND

E4 80	ANDB IND,Y	2  4	LOGICAL AND

E5	BITB IND,X	2  4	BIT TEST

E5 80	BITB IND,Y	2  4	BIT TEST

E6	LDAB IND,X	2  4	LOAD ACCUMULATOR

E6 80	LDAB IND,Y	2  4	LOAD ACCUMULATOR

E7	STAB IND,X	2  4	STORE ACCUMULATOR

E7 80	STAB IND,Y	2  4	STORE ACCUMULATOR

E8	EORB IND,X	2  4	EXCLUSIVE OR

E8 80	EORB IND,Y	2  4	EXCLUSIVE OR

E9	ADCB IND,X	2  4	ADD WITH CARRY

E9 80	ADCB IND,Y	2  4	ADD WITH CARRY

EA	ORAB IND,X	2  4	INCLUSIVE OR

EA 80	ORAB IND,Y	2  4	INCLUSIVE OR

EB	ADDB IND,X	2  4	ADD WITHOUT CARRY

EB 80	ADDB IND,Y	2  4	ADD WITHOUT CARRY

EC	LDD IND,X	2  5	LOAD DOUBLE ACCUMULATOR

EC 80	LDD IND,Y	2  5	LOAD DOUBLE ACCUMULATOR

ED	STD IND,X	2  5	STORE DOUBLE ACCUMULATOR

ED 80	STD IND,Y	2  5	STORE DOUBLE ACCUMULATOR

EE	LDX IND,X	2  5	LOAD INDEX REGISTER X

EE 80	LDX IND,Y++	2  5	LOAD INDEX REGISTER X WITH/Y++

EF	STX IND,X	2  5	STORE INDEX REGISTER X

EF 80	STX IND,X	2  5	STORE INDEX REGISTER X

F0	SUBB EXT	3  4	SUBTRACT

F1	CMPB EXT	3  4	COMPARE

F2	SBCB EXT	3  4	SUBTRACT WITH CARRY

F3	ADDD EXT	3  6	ADD DOUBLE ACCUMULATOR

F4	ANDB EXT	3  4	LOGICAL AND

F5	BITB EXT	3  4	BIT TEST

F6	LDAB EXT	3  4	LOAD ACCUMULATOR

F7	STAB EXT	3  4	STORE ACCUMULATOR

F8	EORB EXT	3  4	EXCLUSIVE OR

F9	ADCB EXT	3  4	ADD WITH CARRY

FA	ORAB EXT	3  4	INCLUSIVE OR

FB	ADDB EXT	3  4	ADD WITHOUT CARRY

FC	LDD EXT	3  5	LOAD DOUBLE ACCUMULATOR

FD	STD EXT	3  5	STORE DOUBLE ACCUMULATOR

FE	LDX EXT	3  5	LOAD INDEX REGISTER X

FF	STX EXT	3  5	STORE INDEX REGISTER X